|  | QUOTATION SCHEDULE B |  |
| --- | --- | --- |

REFERENCE RFQ. TITLE:	SUPPLY, FIT AND DELIVERY OF ONE (1) ONLY ALUMINUM DUMP BODY PACKAGE WITH ALUMINUM CROSS BED TOOLBOX AND CRANE

RFQ No.:			1220-040-2016-117

CONTRACTOR

Legal Name:

Address:

Phone:

Fax:

Email:

CITY OF SURREY

TO:

City Representative:	Richard D. Oppelt, Purchasing Manager

Address:		Surrey City Hall

Finance & Technology Department – Purchasing Section

Reception Counter, 5th Floor West

13450 – 104th Avenue, Surrey, B.C., V3T 1V8

Telephone:		604-590-7274

Email:			purchasing@surrey.ca

1.	The Contractor offers to supply to the City of Surrey the Goods for the prices plus applicable taxes as follows:

Year, Make & Model:  __________________________________________________________

All costs to meet the preferred technical specifications should be included in the following delivered prices.

| UNIT PRICE: (Dump Body Package with Cross Bed Toolbox and Crane including installation costs) | $_______________ X 1 | $________________ |
| --- | --- | --- |
| MANUFACTURER/DEALER DISCOUNT(S): | ($______________) X 1 | ($_______________) |
| SUB-TOTAL: | $______________ |
| GST (5%): | $______________ |
| PST (7%): | $______________ |
| TOTAL QUOTED PRICE: | $_______________ |

Payment Terms:

A cash discount of ________ % will be allowed if the invoices is paid within _______ days, or the ____ day of the month following, or net 30 days, on a best effort basis.

The lowest price of any Quotation received will not necessarily be accepted but will be reviewed to determine the best overall value to the City.

Delivery of Goods:

The completed unit should be delivered within _______ days after receipt of purchase order.

Please complete if applicable:	British Columbia Certified (

PREFERRED SPECIFICATIONS RESPONSE MATRIX (use the spaces provided and/or attach additional pages, if necessary)

SUPPLY, FIT AND DELIVERY OF ONE (1) ONLY ALUMINUM DUMP BODY PACKAGE WITH ALUMINUM CROSS BED TOOLBOX AND CRANE

| PREFERRED SPECIFICATIONS | COMPLIANCE WITH PREFERRED TECHNICAL SPECIFICATIONS YES/NO | MANUFACTURERS’ SPECIFICATIONS OF EQUIPMENT OFFERED. CONTRACTOR SHOULD EXPLAIN ANY DEVIATION WITH THE PREFERRED TECHNICAL SPECIFICATIONS BELOW: |
| --- | --- | --- |

| 1. | BODY MANUFACTURER |
| --- | --- |
| 1.1 | State name of body manufacturer if different from the installer or Contractor | Yes No |  |
| 2. | BODY DIMENSIONS |
| 2.1 | The body, crane, and toolbox should be fitted to a cab & chassis with approximate dimensions of 126 inch CA, | Yes No |  |
| 2.2 | Length – 9’ 4” Outside, 9’ Inside | Yes No |  |
| 2.3 | Width – 96” outside, 88” inside | Yes No |  |
| 2.4 | Side height – 16” | Yes No |  |
| 2.5 | Tailgate Height – 22” | Yes No |  |
| 2.6 | Layout drawings of proposed body, crane and cross bed box should be provided at the time of Quotation. | Yes No |  |
| 2.7 | Mounting of dump body, crane, and tool box shall be done with keeping the clearance between the cab and the box, and the box and the dump body to a minimum, to ensure weight transfer to the front axle | Yes No |  |
| 3. | FLOOR AND UNDERSTRUCTURE |
| 3.1 | Floor should be fabricated from 3/16” aluminum sheet, and the welded joint shall be centre bottom side seam weld to give a smooth interior surface. | Yes No |  |
| 3.2 | Floor sheet should be formed with angle down at the outside edge on both sides to prevent material from hanging up when fold down sides are open. | Yes No |  |
| 3.3 | Rear edge of floor sheet should be reinforced to prohibit defection and maintain a positive, long lasting tailgate seal. | Yes No |  |
| 3.4 | Three (3) flush mount tie downs should be installed on each side of the deck, (front, middle, and rear of deck) | Yes No |  |
| 3.5 | 8” Formed channel longsills | Yes No |  |
| 3.6 | Interlaced 3” I-Beam cross sills, spaced approximately 13.5” on center and reinforced with gussets. | Yes No |  |
| 3.7 | Rear apron should be 8” high, full width design and made with 3/16” aluminum. | Yes No |  |
| 3.8 | Rear apron should include 3 clearance lights to meet CMVSS standards, mounted in shock resistant rubber grommets to maximize bulb life. | Yes No |  |
| 4. | BODY FRONT & SIDES |
| 4.1 | Front should be fabricated from 3/16” aluminum. | Yes No |  |
| 4.2 | Front to be seamless one-piece design with triple bend top rails for long-term durability | Yes No |  |
| 4.3 | Full height front corner posts should include clearance lights at each corner to comply with CMVSS safety standards. | Yes No |  |
| 4.4 | Fold down sides should be 16” high and fabricated from 3/16” aluminum. | Yes No |  |
| 4.5 | Fold down sides should have center mounted single release handles. | Yes No |  |
| 4.6 | Dirt shedding bottom rails are attached with heavy duty double strip greaseable hinges allowing sides to rotate down 180 degrees. | Yes No |  |
| 4.7 | Side design includes fully boxed 45 degree dirt shedding top rail and a 50 degree sloped bottom rail for a completely self-cleaning profile. | Yes No |  |
| 4.8 | Sides are to include (2) 6” wide vertical braces per side, with continuous welds for additional strength. | Yes No |  |
| 4.9 | Full depth rear corner posts should be 11.5” wide and 5” deep with hardware concealed for a clean look. | Yes No |  |
| 4.10 | Sides should be equipped with front and rear 6” board pockets to include 2” x 8” wood sideboards painted black. | Yes No |  |
| 5. | CAB SHIELD |
| 5.1 | Integrated design with dump body front. Should be fabricated from 3/16” aluminum material with slotted viewing window. | Yes No |  |
| 6. | TAILGATE |
| 6.1 | Should be fabricated from 3/16” aluminum with fully boxed dirt-shedding top and bottom rails and incorporated (2) vertical braces to provide additional strength and rigidity. | Yes No |  |
| 6.2 | Tailgate should be a 3 way design, with dump through bottom, lay flat, or lay down. | Yes No |  |
| 6.3 | The lower tailgate release should be operated from inside cab. | Yes No |  |
| 7. | LIGHTS / WIRING |
| 7.1 | All lights and reflectors should meet or exceed CMVSS requirements. | Yes No |  |
| 7.2 | Lights should be LED, flush mounted in shock resistant rubber grommets. | Yes No |  |
| 7.3 | Each rear corner post should include a rear facing auxiliary stop/turn/tail lamp for improved visibility and operator safety. | Yes No |  |
| 8. | HOIST / HYDRAULICS |
| 8.1 | Hoist should be a scissor lift style design, with 9 ton capacity. | Yes No |  |
| 8.2 | Hoist should be powered by single acting electric over hydraulic power pack mounted under box with in cab controls. | Yes No |  |
| 8.3 | PTO/Pump hydraulic system supplied and installed for crane operation. | Yes No |  |
| 9. | CROSS BED TOOLBOX |
| 9.1 | Aluminum cross box should be mounted between dump body and chassis. | Yes No |  |
| 9.2 | Cross box should be 30” wide, with a door opening large enough to allow for the fitment of a CNG tank in the box. The tank should be fitted in the upper most part of the toolbox, leaving space below for tools. The box should have a single door opening each side with an opening of approximately 26”. | Yes No |  |
| 9.3 | The cross box should be of a design and strength to support and accommodate 250lb CNG tank. Tank size is approximately 61” long and 20” in diameter. Body builder should supply and install protective covering to front of tank and lines going down in cross box. The mounting of the tank must be in accordance with relevant regulations and laws. | Yes No |  |
| 9.4 | Cross box should be approx. 60” tall, with a flat bottom to accommodate the mounting of a second CNG tank on drivers side chassis rail. The tank should not interfere with the operation of the crane or other equipment. Contractor to provide details of the layout of the tank. | Yes No |  |
| 9.5 | Cross box should have (3) adjustable shelves inside. | Yes No |  |
| 9.6 | Two (2) 24” Underbody cabinet toolboxes should be mounted to the frame rails, one either side of the truck. | Yes No |  |
| 9.7 | CNG filling port should be located between the cab and the tool box | Yes No |  |
| 10. | CRANE |
| 10.1 | Articulating crane mounted between crossbox and dump box. | Yes No |  |
| 10.2 | State Brand of Crane: | Yes No |  |
| 10.3 | State Model of Crane: | Yes No |  |
| 10.4 | Preferred Minimum Capacity of 5920 lbs @ 8’ | Yes No |  |
| 10.5 | Preferred Minimum Capacity of 3737 lbs @ 13’ | Yes No |  |
| 10.6 | Preferred Minimum Capacity of 2634 lbs @ 18’ | Yes No |  |
| 10.7 | Preferred Minimum Capacity of 2039 lbs @ 23’ | Yes No |  |
| 10.8 | Dual stabilizers with hydraulic up/down. | Yes No |  |
| 10.9 | Preferred Oil Tank capacity of 35L. | Yes No |  |
| 10.10 | Preferred 400 degree slewing angle | Yes No |  |
| 10.11 | Stabilizer should able to swing 180 degrees and stored in upright position | Yes No |  |
| 10.12 | Crane should be made of high textile strength steel. | Yes No |  |
| 10.13 | Crane should have hexagonal booms | Yes No |  |
| 10.14 | Crane should have self-lubricating bushings | Yes No |  |
| 10.15 | Crane should come with swivel load hook | Yes No |  |
| 10.16 | Crane should have a rack and pinion slewing system | Yes No |  |
| 10.17 | Crane should be radio remote control with proportional valves and manual controls on driver side. | Yes No |  |
| 10.18 | Crane should come complete with all engineering paperwork, and 360 degree stability load chart. | Yes No |  |
| 11. | ADDITIONAL BODY FEATURES |
| 11.1 | Class V hitch with 6 pin 1235 BX Cole Hersey t/plug wired to factory brake controller. | Yes No |  |
| 11.2 | Wheelan # R2LPPA amber beacon mounted to center of cab shield wired to factory switch in cab with a direct power feed. | Yes No |  |
| 11.3 | Spring rewind tarping system mounted off of bulkhead (not to interfere with tool holder) Spring rewind tarp should sit on top of bulkhead and not protrude into box. | Yes No |  |
| 11.4 | Aluminum tool holder to be mounted on front bulkhead passenger side (holds min of 6 tools). | Yes No |  |
| 11.5 | Fold down steps on either side of dump package for easy access. | Yes No |  |
| 11.6 | Rigging Rack mounted on cross box beside crane for chains, straps, etc. | Yes No |  |
| 11.7 | Electric tailgate release with switch inside of cab. | Yes No |  |
| 11.8 | Back up alarm Grote part # 73040 97 dBA. | Yes No |  |
| 11.9 | (6) Heavy Duty flush mount tie down “D” Rings in dump body floor. (3) per side. | Yes No |  |
| 12. | WARRANTY |
| 12.1 | Provide details of manufacturer’s warranty – should be a minimum of 1 year | Yes No |  |
| 12.2 | Provide details of installers warranty on workmanship and parts. | Yes No |  |
| 13. | MANUALS |
| 13.1 | One copy of parts manuals (CD-ROM for complete Goods and all added components is preferred). | Yes No |  |
| 13.2 | One copy of service manuals (CD-ROM for complete Goods and all added components is preferred). | Yes No |  |
| 13.3 | One copy of electrical manual with all added wiring system schematics from all added components (CD-ROM for complete Goods and all added components is preferred). | Yes No |  |
| 13.4 | One copy of operator’s manual for Goods and components added (CD-ROM for complete Goods and all added components is preferred). | Yes No |  |
| 14. | PRE-BUILD |
| 14.1 | Prior to acceptance of the Contractor’s Quotation, a meeting may be held with the Contractor to ensure all conditions of this RFQ can be met by the preferred Contractor as to the scope of the specifications. | Yes No |  |

2.	If this Quotation is accepted by the City, a contract will be created as described in:

(a)	the Agreement;

(b)	the Quotation;

(c)	the specifications set out above and in Schedule A of the RFQ; and

(d)	other terms, if any, that are agreed to by the parties in writing.

3.	Capitalized terms used and not defined in this Quotation will have the meanings given to them in the RFQ.  Except as specifically modified by this Quotation, all terms, conditions, representations, warranties and covenants as set out in the RFQ will remain in full force and effect.

4.	I/We have reviewed the RFQ Attachment 1 – Draft Quotation Agreement.  If requested by the City, I/we would be prepared to enter into that Agreement, amended by the following departures (list, if any):

Section			Requested Departure(s) / Alternative(s)

5.	In addition to the warranties provided in the Draft Quotation Agreement, this Quotation includes the following warranties:

6.	I/We have reviewed the RFQ Attachment 1, Schedule A – Specifications of Goods and if requested by the City, I/we would be prepared to meet those requirements, amended by the following departures and additions (list, if any):

Requested Departure(s) / Alternative(s) / Addition(s)

7.	The Contractor’s references (name and telephone number).  The City’s preference is to have a minimum of three (3) references:

8.	I/We the undersigned duly authorized representatives of the Contractor, having received and carefully reviewed the RFQ including without limitation the specifications and the General Terms and Conditions, submit this Quotation in response to the RFQ.

This Quotation is offered by the Contractor this _______ day of _______________, 201_.

CONTRACTOR

I/We have the authority to bind the Contractor

| ________________________________________ (Legal Name of Contractor) _________________________________________ (Signature of Authorized Signatory) _________________________________________ (Print Name and Position of Authorized Signatory) | ________________________________________ (Signature of Authorized Signatory) ________________________________________ (Print Name and Position of Authorized Signatory) |
| --- | --- |

This Quotation is accepted by the City this _______ day of _______________, 201_.

CITY OF SURREY

| ________________________________________ (Signature of Authorized Signatory) _________________________________________ (Print Name and Position of Authorized Signatory) _________________________________________ (Signature of Authorized Signatory) |  |
| --- | --- |

| _________________________________________ (Print Name and Position of Authorized Signatory) |  |
| --- | --- |