|  | SCHEDULE B – FORM OF QUOTATION |
| --- | --- |

RFQ Title:	Supply and Delivery of Three (3) Tractors/Tool Carriers with Sweeper, Sander, Snow Plough, Water Tank, and Water Flusher Attachments

RFQ No:	1220-040-2017-089

CONTRACTOR

Legal Name:

Address:

Phone:

Fax:

Email:

CITY OF SURREY

TO:

City Representative:	Richard D. Oppelt

Purchasing Manager

Address:		Surrey City Hall

Finance & Technology Department – Purchasing Section

Reception Counter, 5th Floor West

13450 – 104th Avenue, Surrey, B.C., V3T 1V8

Telephone:		604-590-7274

Email:			purchasing@surrey.ca

1.	The Contractor offers to supply to the City of Surrey the Goods for the prices plus applicable taxes as follows:

Year, Make & Model:  __________________________________________________________

All costs to meet the preferred specifications should be included in the following delivered prices.

|  | “Without Trade/s” |  |  |
| --- | --- | --- | --- |

| UNIT PRICE: | $________________ X 3 | $______________ |
| --- | --- | --- |
| ENVIRONMENTAL LEVIES: BATTERY: | $________________ X 3 | $______________ |
| TIRE STEWARDSHIP B.C. (TSBC): ADVANCED DISPOSAL FEE (ADF): AIR CONDITIONING: ANY OTHER LEVIES OR FEES: | $________________ X 3 $________________ X 3 $________________ X 3 | $______________ $______________ $______________ |
|  | SUB-TOTAL: | $______________ |
| GST 5% on $ ___________: | HST | $______________ |
| PST 7% on $____________: | HST | $______________ |
| TOTAL QUOTED PRICE: |  | $______________ |

Payment Terms: 
A cash discount of ________ % will be allowed if the invoices are paid within _______ days, or the ____ day of the month following, or net 30 days, on a best effort basis.

The completed unit shall be delivered within _______ days after receipt of purchase order.

Complete Vehicle:  State Warranty (no less than one (1) year)

Extended Warranty Options:  __________________________________________________________________________

Warranty repairs shall be performed at

2.		If this offer is accepted by the City, such offer and acceptance will create a contract as described in:

(a)	the RFQ;

(b)	the specifications set out above and in Schedule A of the RFQ;

(c)	the General Terms and Conditions;

(d)	this Quotation; and

(e)	other terms, if any, that are agreed to by the parties in writing.

3.		Capitalized terms used and not defined in this Quotation will have the meanings given to them in the RFQ.  Except as specifically modified by this Quotation, all terms, conditions, representations, warranties and covenants as set out in the RFQ will remain in full force and effect.

4.	I/We the undersigned duly authorized representatives of the Contractor, having received and carefully reviewed the RFQ including without limitation the Specifications and the General Terms and Conditions, submit this Quotation in response to the RFQ.

This Quotation is offered by the Contractor this _______ day of _______________, 201_.

CONTRACTOR

I/We have the authority to bind the Contractor

| ________________________________________ (Legal Name of Contractor) _________________________________________ (Signature of Authorized Signatory) _________________________________________ (Print Name and Position of Authorized Signatory) | ________________________________________ (Signature of Authorized Signatory) ________________________________________ (Print Name and Position of Authorized Signatory) |
| --- | --- |

This Quotation is accepted by the City this _______ day of _______________, 201_.

CITY OF SURREY

| ________________________________________ (Signature of Authorized Signatory) _________________________________________ (Print Name and Position of Authorized Signatory) _________________________________________ (Signature of Authorized Signatory) | ________________________________________ (Signature of Purchasing Representative ________________________________________ (Print Name of Purchasing Representative) |
| --- | --- |

| _________________________________________ (Print Name and Position of Authorized Signatory) |  |
| --- | --- |

SCHEDULE B-1 – SPECIFICATIONS WORKSHEET

Supply and Delivery of Three (3) Tractors/Tool Carriers with Sweeper, Sander, Snow Plough, Water Tank and Water Flusher Attachments

SPECIFICATIONS

The specification herein states the minimum requirements of the City of Surrey. All Quotations shall be regular in every respect. Unauthorized conditions, limitations, or provisions shall be cause for rejection. The City of Surrey will consider as "irregular" or "non-responsive" any Quotation not prepared and submitted in accordance with the RFQ document and specification, or any Quotation lacking sufficient technical literature to enable the City to make a reasonable determination of compliance to the specification.

It shall be the Contractor's responsibility to carefully examine each item of the specification. Failure to offer a completed Quotation or failure to respond to each section of the technical specification will cause the Quotation to be rejected without review as "non-responsive". All variances, exceptions and/or deviations shall be fully described in the appropriate section.

Note: Contractors are directed to list complete manufacturers’ details of model proposed in the right-side column under manufacturers’ specifications

| Preferred Specifications | √ (Yes) | √ (No) | Manufacturers’ Specifications of Equipment Offered. Contractor shall complete all spaces in this column. |
| --- | --- | --- | --- |
| DIMENSIONS |
| 1.1 Overall length including rear bumper 126" (3200 mm) | □ | □ |  |
| 1.2 Height to top of cab 78" (1981 mm) | □ | □ |  |
| 1.3 Track width (winter tires) 47" (1194 mm) | □ | □ |  |
| 1.4 Overall width with fenders 47” (1194 mm) | □ | □ |  |
| 1.5 Inside Turning Radius 67” (1702 mm) maximum | □ | □ |  |
| 1.6 Articulation angle of 39 degrees each way | □ | □ |  |
| 1.7 Oscillation angle of 7 degrees above and below horizontal. | □ | □ |  |
| 1.8 Ground clearance of 8.75” (222 mm) | □ | □ |  |
| ENGINE |
| 2.1 Four (4) cylinder, diesel, water cooled, engine, minimum 45 HP, minimum torque of 105 lb. ft. @1800 RPM. Shall meet latest engine emission standards, please state | □ | □ |  |
| 2.2 Cold starting aid: block heater and hydraulic oil tank heater | □ | □ |  |
| 2.3 Quick change air filter with pre-cleaner mounted outside of engine compartment. To include service indicator (vacuum gauge) | □ | □ |  |
| 2.4 Buzzer, warning symbol system activated for; low oil pressure or high water temperature. Display to be shown in diagnostic display monitor | □ | □ |  |
| 2.5 Rear engine hood, side panels and grille shall be removable without tools. Once removed, complete engine access shall be available. | □ | □ |  |
| 2.6 Rubber grommets are to be used on both panels and hood to dampen vibration. There shall be access to the engine oil dipstick without removal of any panel. | □ | □ |  |
| 2.7 Throttle to be controlled by hand lever & foot pedal. | □ | □ |  |
| COOLING |
| 3.1 Radiator fan to be protected by steel housing. Shall be able to reach complete radiator area for cleaning. | □ | □ |  |
| 3.2 Shall allow full access to entire cooling surface for cleaning (i.e. bottom area shall allow for full access). | □ | □ |  |
| 3.3 Combined cooler – hydraulic oil and engine coolant. Wide fin, no-barb design to allow maximum air flow and prevent clogging, | □ | □ |  |
| 3.4 Cooling fan shall be pusher-style | □ | □ |  |
| FRAME |
| 4.1 Frame rails shall be of sufficient strength to withstand the rigors of heavy transport while traveling, complete with all front mounted attachments and rear sander combination. | □ | □ |  |
| 4.2 Shall have on-demand ride control operated via a switch. This will allow front 3 point linkage arms to float on a hydraulic accumulator circuit improving travel comfort and safety. | □ | □ |  |
| 4.3 The machine shall be supplied with central greasing system of minimum 0.4gal (1.5L) capacity with display function. | □ | □ |  |
| IMPLEMENT DRIVE |
| 5.1 Shall be hydraulic drive operated by one of two hydraulic circuits, or both. | □ | □ |  |
| 5.2 First circuit to have minimum of 14 gpm (53 litres/min). Second circuit to have 9.5 gpm (36 litres/min). | □ | □ |  |
| 5.3 Provision to use both circuits simultaneously shall be available. | □ | □ |  |
| 5.4 Primary circuit (14 gpm/53 liters/min) to be double-acting (reversible). | □ | □ |  |
| FRONT HITCH |
| 6.1 Front lift system shall consist of a 3 point hitch in compliance with category 1 hitch standards (3/4" top link pin diameter and 7/8" lift arm pin diameter). | □ | □ |  |
| 6.2 There shall be 2 forward extending hitch arms with two category 1 lift hooks. | □ | □ |  |
| 6.3 Lift hooks shall be self-locking and to be un- latchable from the top without tools. | □ | □ |  |
| 6.4 Lift hooks to be slide mounted such that each hook can be slid 6 inches horizontally on hitch arms to adapt to various attachments pin positions. | □ | □ |  |
| 6.5 Top link block shall provide 4 pin off holes for top link angle adjustments | □ | □ |  |
| 6.6 Hitch lift height at attachment forward extension point (i.e. blower and plough cutting edge shall lift to a minimum of 30" (762 mm) clear lift) | □ | □ |  |
| 6.7 Hydraulic lift control to provide feather-ability through a pilot controlled lift circuit. | □ | □ |  |
| 6.8 Front hitch to have switchable ride control using an in line accumulator | □ | □ |  |
| 6.9 Hitch to have latched switch controlled float control | □ | □ |  |
| 6.10 Front hitch arms to be pinned to front frame (not cab base) | □ | □ |  |
| TRANSMISSION |
| 7.1 Ground speed to be controlled in (4) interconnected ways: foot engine throttle, hand throttle, inching dial and foot inching pedal. | □ | □ |  |
| 7.2 A hand-operated inching valve used with the hand throttle, is to be supplied allowing adjustable ground speed to be set for attachment operation. | □ | □ |  |
| 7.3 Transmission may be shifted to neutral, forward, reverse from joystick by activating a switch without removing one’s hand from the joystick. | □ | □ |  |
| 7.4 As a safety precaution, the joystick F/N/R function is to be disabled until the parking brake is released. | □ | □ |  |
| 7.5 Mechanical transmission to be a 1-speed reduction gear and driven by 2-speed hydraulic motor and provide a speed range of: 0 –11 mph (18 km/h) in low and 0-22 mph (36 km/h) in high. | □ | □ |  |
| 7.6 Shall be equipped with a load-sensing drive system which doesn’t allow diesel engine to become overloaded | □ | □ |  |
| 7.7 Rear axle shall be connected to front axle to provide full drive line power and torque to be available in all working conditions. | □ | □ |  |
| 7.8 Drive line shall be located above the center articulation points in the center section. Below mounted drive line not acceptable. | □ | □ |  |
| 7.9 Drive flow hydraulic lines not to cross center section. | □ | □ |  |
| AXLES |
| 8.1 Axles shall be full floating planetary, with limited slip differentials front and rear and automatic lock on front axle. | □ | □ |  |
| 8.2 Rated capacity of each axle shall be approx. 5,100 lbs. (2,320 kgs.) | □ | □ |  |
| BRAKING SYSTEM |
| 9.1 Shall have a minimum of three (3) braking systems (hydrostatic, service and emergency/parking). | □ | □ |  |
| 9.2 Hydrostatic braking through driveline brakes when backing off foot pedal. | □ | □ |  |
| 9.3 Service brakes to be hydraulic actuated drum activing on all four wheels. | □ | □ |  |
| 9.4 Out board brakes not acceptable. | □ | □ |  |
| 9.5 Emergency/parking brake shall be act on all four wheels. | □ | □ |  |
| HUBS, WHEELS AND TIRES |
| 10.1 Industrial 6 bolt pattern with M18 studs. | □ | □ |  |
| 10.2 Supply and install five (5) deep lug radial winter tires to be 6 ply (LT235/75R15), mounted on heavy duty steel wheels. | □ | □ |  |
| 10.3 Industrial wheel rim and center flange with hub pilot centre featuring valve stem protectors. | □ | □ |  |
| 10.4 Valve stems to be protected with weld on stem protection ear. | □ | □ |  |
| HYDRAULIC SYSTEM |
| 11.1 Pump shall have built in priority flow divider to supply power steering | □ | □ |  |
| 11.2 Front of machine shall be equipped with two (2) pairs of function (auxiliary couplers), one (1) 14gpm (53 litres/min), (1) 9.5gpm (36 litres/min) coupler and a case drain coupler. | □ | □ |  |
| 11.3 Rear of machine shall be equipped with one (1) pair 14gpm (53 litres/min) motor spool couplers with case drain and (1) pair of auxiliary couplers. | □ | □ |  |
| 11.4 Hydraulic pressurized oil fill top up system through tank filter. No reservoir free pour access port to be provided. | □ | □ |  |
| 11.5 External hydraulic tank oil level indicator glass | □ | □ |  |
| 11.6 All cylinders feature self-aligning spherical bearing body and rod ends (long life feature) | □ | □ |  |
| 11.7 All hydraulic pumps to be driven on the fly wheel end of engine only. | □ | □ |  |
| ELECTRICAL |
| 12.1 12 Volt DC, negative ground with a 650cca, group 31 battery, 65 amp alternator & voltmeter, battery disconnection switch protection. | □ | □ |  |
| 12.2 An emergency stop button to be included, mounted on dash panel | □ | □ |  |
| 12.3 Fuses to be mounted behind dash console. Fuse/relay diagram decal to be placed on inside cover. | □ | □ |  |
| 12.4 Switches and dials for lights, heater, A/C, parking brake, heated mirrors to be mounted on dash in group formation | □ | □ |  |
| 12.5 Supply and install low hydraulic oil level light and buzzer | □ | □ |  |
| 12.6 Illuminated display monitor showing the following: Warning for low hydraulic oil level Tachometer / hour meter Coolant temperature Engine oil pressure w/ signal light Hydraulic oil temperature Voltmeter Fuel level | □ | □ |  |
| LIGHTING |
| 13.1 There shall be two (2) headlights, four (4) forward and two (2) rearward facing work lights, all to be mounted at top of cab. Two backup lights shall operate with reverse switch and on- demand via dash rocker switch. | □ | □ |  |
| 13.2 There shall be two rear rubber-mounted combination tail/signal lights | □ | □ |  |
| 13.3 There shall be four way “hazard” flashers and self-cancelling turn signals | □ | □ |  |
| 13.4 A rubber based warning beacon with breakaway mount shall be provided | □ | □ |  |
| CAB |
| 14.1 The cab shall be “ROPS Certified” to ISO- 3471 specifications and bear a certification label | □ | □ |  |
| 14.2 Cab shall be rubber isolation mounted (cab shall not be ride mounted or integrated to front frame) | □ | □ |  |
| 14.3 Cab to feature one left side opening forward swinging door with left side sliding window | □ | □ |  |
| 14.4 Door hinges to have individual grease nipples and replacement brass hinge carry washers | □ | □ |  |
| 14.5 Noise level to be 73-74 DBA inside at max engine rev. | □ | □ |  |
| 14.6 Cab glass to be mounted to bolted (not glued) aluminum sub frames for quick exchange | □ | □ |  |
| 14.7 Mirror to be mounted in cab frame (not door) using adjustable friction mounts to hold mirror position but allow swing away protection | □ | □ |  |
| 14.8 Mirrors to be heated | □ | □ |  |
| 14.9 Cab heat vents shall be placed in 4 positions within the cab interior | □ | □ |  |
| 14.10 At the entire front windshield base area from left to right in the form of a manifold with 10 or more openings | □ | □ |  |
| 14.11 Side window defrosting in the cab “B” pillars left and right with adjustable vents | □ | □ |  |
| 14.12 Floor heating vents that have adjustable air flow direction and rate | □ | □ |  |
| 14.13 Air fan shall be 3 speed or variable flow | □ | □ |  |
| 14.14 Top headliner located defrost vents not acceptable. | □ | □ |  |
| 14.15 A separate air recirculation control shall all from 0-100% of air to recirculate or provide full pressurization | □ | □ |  |
| 14.16 Air intake shall be filtered with a replaceable paper element | □ | □ |  |
| 14.17 Separate recirculation air filters (replaceable) shall be included separately from intake filter system | □ | □ |  |
| 14.18 Right side window to have a full opening swing out feature for training and operator emergency egress | □ | □ |  |
| 14.19 Cab wipers to be pantograph front, featuring grease and rear with separate controls and washer systems. | □ | □ |  |
| 14.20 Front pantograph wiper arms to have long life wiper blade bushings with refillable grease caps. | □ | □ |  |
| 14.21 Beacon lights to be DIN post mounted with swing down features | □ | □ |  |
| 14.22 Red stop button dash mounted for driver emergency shut down | □ | □ |  |
| Cab to contain: Horn 3 Speed heater defroster 2 Speed pantograph wiper with intermittent control Windshield washer Floor mats Inside rear view mirror Exterior heated mirrors Dome lights with blue and/or white lighting 2 Point seat belt Sound absorption lining AM/FM/CD Radio, mounted overhead Tilt steering in column Removable door and side panel Flat step for safe entry Heated, air-ride operator seat Overhead roof window Air-conditioner with cab pressurizer below roof line and extra heat to be controlled on the dash panel Supply and install guard for headlight protection Rear mounted windshield wiper/washer Sun visor Flat floor with no drive line hump | □ | □ |  |
| SEAT |
| 15.1 Heated, air auto adjusting seat for drivers weight | □ | □ |  |
| 15.2 Air lumbar and bolster adjustments | □ | □ |  |
| 15.3 Right side adjustable arm rest integrated for wrist position support for right side mounted joy stick | □ | □ |  |
| JOY STICK |
| 16.1 True pilot controlled joy stick control (electronic joy stick not acceptable) | □ | □ |  |
| 16.2 Joy stick is seat mounted such that the operator and joystick move together on the same suspension | □ | □ |  |
| 16.3 4 line hydraulic pilot control system from base of joy stick piped to joy stick pilot valve below the cab floor then controls main high pressure valve mounted to machine frame (cab mounting not acceptable) | □ | □ |  |
| 16.4 Pilot control valve to function at low pressure then activating main valve at full working pressure and flows | □ | □ |  |
| 16.5 Joy stick to have 4 way adjustment stick up, down, forward and backward adjustment | □ | □ |  |
| 16.6 True seat mounting of joy stick (console or dash mounted not acceptable) | □ | □ |  |
| STEERING |
| 17.1 Two double acting steering cylinders operate the articulated steering system | □ | □ |  |
| 17.2 Priority flow at low system pressures to provide safe independent oil pressure to steering cylinders | □ | □ |  |
| 17.3 Steering cylinders to feature rod and body pivot ends to be replaceable, spherical, self- aligning bearing ends with captive pin ends | □ | □ |  |
| 17.4 Steering pins to be tempered with upper and lower wedge pin mounts that prevents frame housing wear | □ | □ |  |
| 17.5 Individual grease lines to be mounted to all four ends of cylinder bearing | □ | □ |  |
| 17.6 Articulation steering bump stops to be designed not to allow steering cylinders to bottom out at steering angle limits (cylinder protection feature) | □ | □ |  |
| WATER PUMP |
| 18.1 All hoses, wiring, switch and quick coupler shall be installed for future optional water/chemical pump. | □ | □ |  |
| FUEL TANK |
| 19.1 Single fuel tank with lockable fuel cap to be supplied. | □ | □ |  |
| 19.2 Shall have 13.0 gal. (50L) minimum capacity. | □ | □ |  |
| SPREADER ATTACHMENT |
| 20.1 Spreader to be constructed of galvanized steel | □ | □ |  |
| 20.2 Spreader to be hook-mounted to rear of carrier requiring no tools for installation or dismantling. Shall be self-loading. | □ | □ |  |
| 20.3 Shall be hydraulically driven with engagement from within cab. | □ | □ |  |
| 20.4 Engagement and disengagement shall be independent from front mounted attachments. | □ | □ |  |
| 20.5 Minimum 1/3 cu.yd. capacity. | □ | □ |  |
| 20.6 Spread shall be by means of a roller with cams which disperses small spots of material in a grid pattern. | □ | □ |  |
| 20.7 Spread distance per hopper load shall be 5-8 kms (3-5 miles). | □ | □ |  |
| 20.8 2 Storage legs/stands to be provided, pin- mounted on the spreader to aid in removal and keep the spreader upright when stored. | □ | □ |  |
| 20.9 Shall have a total width of 44” and a spread width of approximately 41 inches. | □ | □ |  |
| 20.10 Shall have colour coded, 3/4' female hydraulic quick couplers. | □ | □ |  |
| 20.11 Ground clearance to be not less than 12 inches. | □ | □ |  |
| 20.12 Hopper to have a plastic cover. | □ | □ |  |
| 20.13 Agitator to have 11 bolts, 12mm (1/2") x 13cm (5"), rotating on a 4cm (1.5") square shaft. | □ | □ |  |
| 20.14 Delivery roller to be minimum 11.5 cm (4.5") in diameter with 4mm full-length cams | □ | □ |  |
| 20.15 Hydraulic drive motor to be located in upper left hand corner of hopper (when raised) so as to be protected when loading. | □ | □ |  |
| 20.16 An adjustable hydraulic flow valve shall be supplied on spreader frame. This will allow for fine adjustment of spreading rate. | □ | □ |  |
| 20.17 The agitator and roller chain shall be on left hand side of spreader and enclosed with a steel cover. | □ | □ |  |
| 20.18 Grease fittings shall be easily accessible from both sides of spreader body. | □ | □ |  |
| 20.19 Bolt on protective screen shall be installed. Hole size shall be maximum 2"x1.5". | □ | □ |  |
| 20.20 Minimum required dimensions to be 44" wide x 31" high x 21" deep. | □ | □ |  |
| SWEEPER ATTACHMENT |
| 21.1 3 point hitch, Cat.1 mount | □ | □ |  |
| 21.2 Maximum working width of 140cm (55") | □ | □ |  |
| 21.3 Shall have the ability to hydraulically angle left and right a minimum of 27 degrees in each direction. | □ | □ |  |
| 21.4 Shall have the ability to hydraulically side shift a minimum to the left 21.5cm (8.5") and to the right 26.5cm (10.5"). This will allow material removal along an object (wall, fence, etc.) while keeping carrier away from the object. | □ | □ |  |
| 21.5 Brush shall be able to remain straight or angled left/right when side shifted. Operation of angling, side shifting and lifting to be done via joystick control. | □ | □ |  |
| 21.6 The brush drive shall be hydraulic, from a source of maximum 50L/min (13.2 gpm) at 190 bar (2750 psi) | □ | □ |  |
| 21.7 The hydraulic motor shall be center mounted to avoid contact with any objects | □ | □ |  |
| 21.8 Replacing the bristles shall be easily done by removing a tapered nut and retaining flange from each side. Individual brush wafers and spacers are to be mounted on the brush core. | □ | □ |  |
| 21.9 The brush material is to be all poly. | □ | □ |  |
| 21.10 Brush diameter to be a maximum of 70cm (28"). | □ | □ |  |
| 21.11 There shall be three retractable storage stands designed to remain attached to brush frame while in use. | □ | □ |  |
| 21.12 The weight of the entire brush and frame shall be Approximately 320kg (704 lbs.). | □ | □ |  |
| 21.13 Mounting frame designed to "pull" brush along surface. | □ | □ |  |
| 21.14 A shock absorber shall be provided to keep brush in constant contact with surface. | □ | □ |  |
| 21.15 Top and Lower pendulum bars to be provided along with spring loaded adjustment bolts which allows brush to follow uneven terrain. | □ | □ |  |
| 21.16 A spray bar with (4) 110 degree nozzles at 12" spacing and diverter block shall be supplied. Brass quick coupler to be included. | □ | □ |  |
| 21.17 A shield shall be installed covering approximately 50 % of the brush circumference. | □ | □ |  |
| 21.18 All hydraulic hoses to be equipped with colour-coded, 3/4" female couplers. | □ | □ |  |
| 21.19 150L water tank built into broom design | □ | □ |  |
| 21.20 Water tank shall have drain valve | □ | □ |  |
| PLOUGH ATTACHMENT |
| 22.1 3 point Cat 1 hitch mount. | □ | □ |  |
| 22.2 Shall have minimum angling of 28 degrees in each direction. | □ | □ |  |
| 22.3 Expandable width to be from minimum 130 cm (51") closed to minimum 210 cm (83") fully open. | □ | □ |  |
| 22.4 The plough shall be able to expand both left hand and right hand sides simultaneously or either side independently. | □ | □ |  |
| 22.5 All plough functions are to be controlled from the joystick. | □ | □ |  |
| 22.6 Cutting edge to be 12mm (0.5") thick and made from Hardox 400 steel. The edge shall be mounted vertically and be serrated to cut and scrape through compacted snow and ice conditions. | □ | □ |  |
| 22.7 Blade height to be a minimum 60 cm (24"). | □ | □ |  |
| 22.8 Plough weight to be approximately 310 kg (682 lbs.). | □ | □ |  |
| 22.9 Plough assembly shall have full trip capability. Adjustable heavy-duty spring to be provided for this function. | □ | □ |  |
| 22.10 Ten (10) plough mounted onto frame to be adjustable via 2 hole locations, floatation slots designed to provide mechanical oscillation. | □ | □ |  |
| 22.11 Plough shall have end plates to contain material, if so desired. These can be manually raised/lowered and latched or can be swung hydraulically. | □ | □ |  |
| 22.12 A solenoid valve body shall be provided and located on upper plough frame for easy access and trouble shooting. | □ | □ |  |
| 22.13 Power source for solenoid valve to be via 7 pin round plug mounted on exterior front panel of tractor. Engagement from operator's seating position. | □ | □ |  |
| 22.14 All hydraulic hoses to be equipped with colour-coded, 3/4" female couplers. | □ | □ |  |
| WATER TANK ATTACHMENT |
| 23.1 Rear, over-engine tank mounting to be provided, tank overall height shall not exceed roof height. | □ | □ |  |
| 23.2 Pin-mounted steel frame will support the tank and pump and provide clearance to gain engine access. | □ | □ |  |
| 23.3 Tank capacity shall be min. 550L (145 US gal). | □ | □ |  |
| 23.4 There shall be running, directional and brake lights mounted at the rear on both sides of tank frame. | □ | □ |  |
| 23.5 Tank to be constructed of roto-molded polyethylene and designed with interior baffles. | □ | □ |  |
| 23.6 Dual element filtration shall be located in the tank to provide clean water for high pressure pump. | □ | □ |  |
| 23.7 A hydraulically driven, twin piston pump shall be provided. The pump shall have a minimum 130 bar (1,885 psi) working pressure rating and a water flow rating of 30L/min (8 US gal). A manual bypass valve shall be supplied. | □ | □ |  |
| 23.8 Minimum hydraulic flow required for pump operation is 40L/min (10.5 US gal) @ 2,000 RPM. This flow shall be available on the carrier and couplers are to be located at the rear, right side of the vehicle. | □ | □ |  |
| 23.9 Hydraulic flow engagement to be in-cab via rocker switch on right hand side console. | □ | □ |  |
| 23.10 A high pressure water line with brass couplers shall be provided and routed through the articulation of the vehicle. Both ends of the water line to be easily accessed. | □ | □ |  |
| 23.11 The pump water supply port shall act as the tank drain. The port will be located at the bottom and near the front right corner of the tank. | □ | □ |  |
| 23.12 A 2” quick-fill port shall be available and mounted at the top of the tank. A 6m (20’) hose with same fitting will be supplied. | □ | □ |  |
| 23.13 A plastic sight gauge tube to be supplied on the front right corner of the tank. | □ | □ |  |
| 23.14 Four (4) adjustable support stands shall be supplied so vehicle can be driven out from under the tank when stored. | □ | □ |  |
| 23.15 A slow moving sign to be mounted on the rear tank frame. | □ | □ |  |
| FLUSHER ATTACHMENT |
| 24.1 Shall be 3-point hitch mounted | □ | □ |  |
| 24.2 Front spray bar to be 53” in width with an overall spray pattern of 60”. | □ | □ |  |
| 24.3 Six (6) nozzle bodies to be provided with stainless steel nozzle # 02 tips | □ | □ |  |
| 24.4 Fan spray pattern to be 65 degrees |  |  |  |
| 24.5 The spray boom shall be hydraulically angled, controlled via cab joystick | □ | □ |  |
| 42.6 Two (2) adjustable support stands are to be supplied for storage | □ | □ |  |
| 24.7 A built-in counterweight shall be part of the front spray system. This counterweight shall have a min. weight of 240kg (528 lbs.). | □ | □ |  |
| 24.8 A retractable, front-mounted hose reel shall be supplied complete with 15m (50’) of ½“ hose and high pressure hand wand. The hose shall have a pressure rating of 275 bar (4000 psi). | □ | □ |  |
| 24.9 The hose reel shall have the ability to swing 180 degrees and be locked in various positions. | □ | □ |  |
| 24.10 The valve allowing the operator to divert from spray boom to hand gun shall be located at the front and near the hose reel. | □ | □ |  |
| MISCELLANEOUS |
| 25.1 Shop service, parts information, technical | □ | □ |  |
| 25.2 Service bulletins (TSB’s) SHALL be provided electronically by the authorized dealer - NO EXCEPTIONS | □ | □ |  |
| 25.3 Units shall be supplied licensed, plated and insured, done through the City of Surrey’s broker | □ | □ |  |
| 25.4 Units shall meet all applicable transport regulations, both Federal and Provincial, and be permitted to be driven on roads. | □ | □ |  |
| 25.5 Provide details of warranty for all components | □ | □ |  |

– END OF PAGE –