|  | QUOTATION SCHEDULE B |  |
| --- | --- | --- |

RFQ Title:	Supply & Delivery of One (1) Used Loader

RFQ No:	1220-040-2016-105

CONTRACTOR

Legal Name:

Address:

Phone:

Fax:

Email:

CITY OF SURREY

TO:

City Representative:	Richard D. Oppelt

Purchasing Manager

Address:		Surrey City Hall

Finance & Technology Department – Purchasing Section

Reception Counter, 5th Floor West

13450 – 104th Avenue, Surrey, B.C., V3T 1V8

Telephone:		604-590-7274

Email:			purchasing@surrey.ca

1.	The Contractor offers to supply to the City of Surrey the Goods for the prices plus applicable taxes as follows:

Year, Make & Model:  __________________________________________________________

All costs to meet the preferred specifications should be included in the following delivered prices.

| F.O.B. | Payment Terms: | Ship Via: |
| --- | --- | --- |
| Destination Freight Prepaid | A cash discount of ____% will be allowed if invoices are paid within ___ days, or the ___ day of the month following, or net 30 days, on a best effort basis. |  |
| ITEM | One (1) Used Loader |
| UNIT PRICE |  |  |  | $__________ |
| ENVIRONMENTAL LEVY [BATTERY] |  |  |  | $__________ |
| TIRE STEWARDSHIP B.C. (TSBC) |  |  |  | $__________ |
| OTHER: |  |  |  |  |
| ____________________________ |  |  |  | $__________ |
| ____________________________ |  |  |  | $__________ |
| ____________________________ |  |  |  | $__________ |
| SUBTOTAL |  |  |  | $__________ |
| GST 5% |  |  |  | $__________ |
| PST 7% |  |  |  | $__________ |
| TOTAL QUOTED PRICE: |  |  |  | $__________ |
| CURRENCY: CANADIAN |  |  |  |  |

The completed unit shall be delivered within _______ days after receipt of purchase order.

Complete Vehicle:  State Warranty (no less than one (1) year)

Extended Warranty Options:  ___________________________________________________

Warranty repairs shall be performed at

2.		If this offer is accepted by the City, such offer and acceptance will create a contract as described in:

(a)	the RFQ;

(b)	the specifications set out above and in Schedule A of the RFQ;

(c)	the General Terms and Conditions;

(d)	this Quotation; and

(e)	other terms, if any, that are agreed to by the parties in writing.

3.		Capitalized terms used and not defined in this Quotation will have the meanings given to them in the RFQ.  Except as specifically modified by this Quotation, all terms, conditions, representations, warranties and covenants as set out in the RFQ will remain in full force and effect.

4.	I/We the undersigned duly authorized representatives of the Contractor, having received and carefully reviewed the RFQ including without limitation the Specifications and the General Terms and Conditions, submit this Quotation in response to the RFQ.

This Quotation is offered by the Contractor this _______ day of _______________, 201_.

CONTRACTOR

I/We have the authority to bind the Contractor

| ________________________________________ (Legal Name of Contractor) _________________________________________ (Signature of Authorized Signatory) _______________________________________ (Print Name and Position of Authorized Signatory) | ________________________________________ (Signature of Authorized Signatory) ______________________________________ (Print Name and Position of Authorized Signatory) |
| --- | --- |

This Quotation is accepted by the City this _______ day of _______________, 201_.

CITY OF SURREY

| ________________________________________ (Signature of Authorized Signatory) _________________________________________ (Print Name and Position of Authorized Signatory) _________________________________________ (Signature of Authorized Signatory) | ________________________________________ (Signature of Purchasing Representative ________________________________________ (Print Name of Purchasing Representative) |
| --- | --- |

| _________________________________________ (Print Name and Position of Authorized Signatory) |  |
| --- | --- |

RDO Revision May 2016

MAY 21, 2009 U:\LEGALSRV\LEGAL\AGREEMENTS\RFP-Contract-Templates\Documents\Request for Quotations for Goods.doc

saw\lb1-9/29/16 10:03 AM

SCHEDULE B – ATTACHMENT NO. 1 – PREFERRED SPECIFICATIONS

PREFERRED SPECIFICATIONS FOR:  SUPPLY AND DELIVERY OF ONE USED LOADER

Contractor should list complete manufacturer’s details in the right column opposite to the preferred listed requirement.

| Preferred Specifications | Yes (Circle) | No (Circle) | Manufacturers’ Specifications of Equipment Offered. Contractor to indicate compliance or deviation with specifications below. |
| --- | --- | --- | --- |
| General Specifications |
| 1.1 The machine shall be no older than 2012 | Y | N |  |
| 1.2 The machine shall have no more than 8000 hours of operation – provide hour meter reading | Y | N |  |
| 1.3 Tire shall have a minimum of 60% of rubber remaining – provide details | Y | N |  |
| 1.4 The machine shall be supplied with a LoadRite weigh system (L2180 model) with printer | Y | N |  |
| 1.5 Machine shall be supplied with work lights and flood lights | Y | N |  |
| 1.6 A full mechanical inspection report including oil sampling results shall be included in the submission, along with photos of the proposed machine | Y | N |  |
| 1.7 Details of the machines previous work environment shall be provided | Y | N |  |
| 1.8 Operating weight shall be approx. 42,000lbs | Y | N |  |
| 1.9 Machine shall have a 4.5 yd general purpose bucket with bolt on cutting edge | Y | N |  |
| 1.10 Machine shall have a Remote Monitoring System | Y | N |  |
| Preferred Specifications |
| Provide make and model details |
| Engine |
| 3.1 6 cylinder turbo charged, with a minimum of 230 hp gross power | Y | N |  |
| 3.2 Gross peak torque minimum 760 ft-lb | Y | N |  |
| 3.3 Meets of exceeds Interim Tier 4 engine emission standards | Y | N |  |
| Power Train |
| 4.1 The transmission shall be autoshift with torque converter with 4 forward speeds and 4 reverse speeds | Y | N |  |
| 4.2 Maximum forward speed shall be a minimum of 37 km/h | Y | N |  |
| 4.3 Maximum reverse speed shall be a minimum of 39 km/h | Y | N |  |
| 4.4 Front axle shall be fixed, and rear axle shall be oscillating | Y | N |  |
| 4.5 Brakes shall meet OSHA SAE J1473 | Y | N |  |
| 4.6 Machine shall be equipped with emergency steering | Y | N |  |
| Cab |
| 5.1 Unit shall be equipped with 4 post ROPS delux cab | Y | N |  |
| 5.2 3" seat belt shall be provided | Y | N |  |
| 5.3 Unit shall be equipped with illuminated gauges with audible warning for: engine coolant temperature, transmission oil temperature and fuel level. | Y | N |  |
| 5.4 Unit shall have a display for: engine rpm, engine hours, system voltage. | Y | N |  |
| 5.5 The machine will have a cab air conditioner | Y | N |  |
| 5.6 Machine will have lockable storage inside of the cab | Y | N |  |
| 5.7 The seat shall be a cloth suspension type, with fully adjustable armrests and lumbar support. | Y | N |  |
| 5.8 The machine shall have two external mounted mirrors (one either side), and rear vision camera with screen mounted above operator | Y | N |  |
| 5.9 The machine shall have an AM/FM radio fitted |  |  |  |
| Loader |
| Bucket capacity of 4.5 yds, general purpose bucket | Y | N |  |
| 6.2 Bucket lift height shall be no less than 13’ | Y | N |  |
| 6.3 Bucket breakout force shall be no less than 36,000 lb | Y | N |  |
| 6.4 The loader shall have hydraulic self-leveling and bucket-level indicator. | Y | N |  |
| 6.5 A single lever with integrated proportional electrohydraulic control of loader operation | Y | N |  |
| 6.7 The loader shall have a non-removable, loader boom service lock. | Y | N |  |
| 6.8 The bucket shall have bolt on cutting edge with a minimum of 70% life remaining | Y | N |  |
| Warranty |
| 7.1 Proponent to provide details of warranty coverage | Y | N |  |
| Safety |
| 8.1 Machine shall be supplied with, audible back up alarm 98 dbh, Amber LED strobe light wired with its own switch, | Y | N |  |