|  | QUOTATION SCHEDULE B |
| --- | --- |

RFQ Title:	SUPPLY AND DELIVERY OF ONE (1) DUAL FUEL (CNG & GASOLINE) 22,000LB COMMERCIAL STRIP CHASSIS WITH SPECIALIST ITB BODY

RFQ No:	1220-040-2018-076

CONTRACTOR

Legal Name:

Contact Person and Title:

Business Address:

Business Telephone:

Business Fax:

Business E-Mail Address:

CITY OF SURREY

TO:

City Representative:	Richard D. Oppelt

Purchasing Manager

Address:		Surrey City Hall

Finance Department – Purchasing Section

Reception Counter, 5th Floor West

13450 – 104th Avenue, Surrey, BC  V3T 1V8

Telephone:		604-590-7274

Email:			purchasing@surrey.ca

1.	The Contractor offers to supply to the City of Surrey the Goods for the prices plus applicable taxes as follows:

ONE (1) DUAL FUEL (CNG & GASOLINE) 22,000LB COMMERCIAL STRIP CHASSIS WITH SPECIALIST ITB BODY

Year, Make & Model:  __________________________________________________________

All costs to meet the preferred specifications shall be included in the following delivered prices.

| F.O.B. | Payment Terms: | Ship Via: |
| --- | --- | --- |
| Destination Freight Prepaid | A cash discount of ____% will be allowed if invoices are paid within ___ days, or the ___ day of the month following, or net 30 days, on a best effort basis. |  |
| ITEM | ONE (1) DUAL FUEL (CNG & GASOLINE) 22,000LB COMMERCIAL STRIP CHASSIS WITH SPECIALIST ITB BODY |
| CHASSIS PRICE |  |  |  | $________ |
| BODY PRICE |  |  |  | $________ |
| ENVIRONMENTAL LEVY [BATTERY] |  |  |  | $________ |
| TIRE STEWARDSHIP B.C. (TSBC) |  |  |  |  |
| OTHER: |  |  |  | $________ |
| ____________________________ |  |  |  | $________ |
| ____________________________ |  |  |  | $________ |
| SUBTOTAL |  |  |  | $________ |
| GST 5% |  |  |  | $________ |
| PST 7% |  |  |  | $________ |
| TOTAL QUOTED PRICE: |  |  |  | $________ |
| CURRENCY: CANADIAN |  |  |  |  |

The completed unit shall be delivered within _______ days after receipt of purchase order.

Manufacturer’s Warranty:  State Warranty

Body Warranty:  State Warranty________________________________________________

Warranty repairs shall be performed at

Please complete if applicable:	British Columbia Certified (

SPECIFICATIONS

The specification herein states the preferred requirements of the City of Surrey. All Quotations are regular in every respect. Unauthorized conditions, limitations, or provisions shall be cause for rejection. The City of Surrey will consider as "irregular" or "non-responsive" any Quotation not prepared and submitted in accordance with the RFQ document and specification, or any Quotation lacking sufficient technical literature to enable the City to make a reasonable determination of compliance to the specification.

It shall be the Contractor's responsibility to carefully examine each item of the specification. Failure to offer a completed Quotation or failure to respond to each section of the technical specification may cause the Quotation to be rejected without review as "non-responsive". All variances, exceptions and/or deviations shall be fully described in the appropriate section.

Note: Contractors are directed to list complete manufacturers’ details of model proposed in the right-side column under manufacturers’ specifications

| Preferred Specifications | √ (Yes) | √ (No) | Manufacturers’ Specifications of Equipment Offered. Bidder shall complete all spaces in this column. |
| --- | --- | --- | --- |
| Exterior |
| 1.1 Chassis 22,000lbs GVWR | □ | □ |  |
| 1.2 178” wheel base with dual rear wheels | □ | □ |  |
| 1.3 7,700lbs trailer capacity, wiring to match 6 pin 1235 BX Cole Hersey t/plug and brake controller | □ | □ |  |
| 1.4 Galvanized chassis frame – 50KSI yield strength | □ | □ |  |
| Engine |
| 2.1 Engine shall be prepared (gaseous prep engine) to run on CNG and gasoline, and shall comply with all Provincial and Federal engine emission regulations | □ | □ |  |
| 2.2 State engine configuration, size | □ | □ |  |
| 2.3 Full manufactures warranty with CNG conversion should be provided | □ | □ |  |
| 2.4 Cooling system to -30F | □ | □ |  |
| 2.5 CNG system to be integrated into manufacturer’s engine management system. Only factory approved conversions will be acceptable | □ | □ |  |
| 2.6 A/C package | □ | □ |  |
| Transmission, Brakes |
| 3.1 Automatic transmission, state number of speeds | □ | □ |  |
| 3.2 Transmission with tow/haul mode and transmission oil cooler | □ | □ |  |
| 3.3 Power assisted ABS brakes | □ | □ |  |
| Fuel Tanks |
| 4.1 The manufacturers gasoline fuel tank shall remain | □ | □ |  |
| 4.2 CNG tank(s) shall be a size of at least 24.5 GGE/93GLE to give sufficient operating range under normal operating conditions and shall be made of composite material – steel tanks are unacceptable. State tank size | □ | □ |  |
| 4.3 Fuel gauge for each fuel type shall be provided in easy view for the driver | □ | □ |  |
| 4.4 The switch to change from one fuel to the other shall be hidden from the driver | □ | □ |  |
| 4.5 CNG fuel tank(s) to be mounted on the driver’s side chassis rail, in such a manner not to interfere with storage compartments on the body. CNG installer to discuss ITB, chassis supplier and the City of Surrey for the best location | □ | □ |  |
| 4.6 CNG filling port location to be decided with ITB and the City of Surrey | □ | □ |  |
| 4.7 Valving shall be installed in a suitable location to allow for the CNG system to be de-fueled should the need arise | □ | □ |  |
| Wheels, Tires |
| 5.1 Wheels, 6 steel 19.5” x 6.75” | □ | □ |  |
| 5.2 Tires, Highway 245/70Rx19.5 BSW | □ | □ |  |
| Miscellaneous |
| 6.1 Back up alarm - Grote part # 73040 97 dBA | □ | □ |  |
| 6.2 Fire extinguisher 2.5lb dry powder ABC type | □ | □ |  |
| 6.3 WCB Level 1 Basic First Aid Kit | □ | □ |  |
| 6.4The vehicle shall be rust proofed with a product that provides long term protection, and does not require continued reapplication of the product. Contractor to provide details of product offered and warranty. | □ | □ |  |
| 6.5 The Contractor shall deliver the vehicles, registered, insured, and plated as per the City’s insurance requirements through the City’s insurance broker. | □ | □ |  |
| CNG |
| 7.1 The vehicles shall default to run on CNG, and shall only operate on gasoline when the CNG tanks are empty. Vehicles may start on gasoline but should automatically switch to CNG once they reach operating temperature. (Please provide details) | □ | □ |  |
| Warranty |
| 8.1 Provide details of manufacturer’s warranty | □ | □ |  |
| 8.2 Operators Manuals / Service Manuals 1 – Service manual or CD c/w software A build sheet shall be provided detailing (but not limited to the following): VIN Engine details including serial number Transmission details including serial number Diff details including serial number Oil types and quantities for all components Tire make, type and size Engine belts details Filter list for all components Battery details Beacon light make Body drawings, including wiring, plumbing etc. | □ | □ |  |
| 9. Body Package |
| 9.1 ITB Body Quote # 39305 | □ | □ |  |

2.	In addition to the warranties provided in the Draft Quotation Agreement, this Quotation includes the following warranties:

3.	I/We have reviewed the RFQ Attachment 1, Schedule A – Specifications of Goods and if requested by the City, I/we would be prepared to meet those requirements, amended by the following departures and additions (list, if any):

Requested Departure(s) / Alternative(s) / Addition(s)

The City is not obligated to accept any alternatives. The City will determine what constitutes acceptable deviations and overall best value.

4.	If this Quotation is accepted by the City, a contract will be created as described in:

(a)	the Agreement;

(b)	the RFQ; and

(c)	other terms, if any, that are agreed to by the parties in writing.

5.		Capitalized terms used and not defined in this Quotation will have the meanings given to them in the RFQ.  Except as specifically modified by this Quotation, all terms, conditions, representations, warranties and covenants as set out in the RFQ will remain in full force and effect.

6.	I/We have reviewed the RFQ Attachment 1 – Draft Quotation Agreement.  If requested by the City, I/we would be prepared to enter into that Agreement, amended by the following departures (list, if any):

Section			Requested Departure(s) / Alternative(s)

7.	I/We the undersigned duly authorized representatives of the Contractor, having received and carefully reviewed the RFQ including without limitation the specifications and the General Terms and Conditions, submit this Quotation in response to the RFQ.

This Quotation is offered by the Contractor this _______ day of _______________, 201_.

CONTRACTOR

I/We have the authority to bind the Contractor

| ________________________________________ (Legal Name of Contractor) _________________________________________ (Signature of Authorized Signatory) _________________________________________ (Print Name and Position of Authorized Signatory) | ________________________________________ (Signature of Authorized Signatory) ________________________________________ (Print Name and Position of Authorized Signatory) |
| --- | --- |

This Quotation is accepted by the City this _______ day of _______________, 201_.

CITY OF SURREY

| ________________________________________ (Signature of Authorized Signatory) _________________________________________ (Print Name and Position of Authorized Signatory) _________________________________________ (Signature of Authorized Signatory) | ________________________________________ (Signature of Purchasing Representative ________________________________________ (Print Name of Purchasing Representative) |
| --- | --- |

| _________________________________________ (Print Name and Position of Authorized Signatory) |  |
| --- | --- |