|  | QUOTATION SCHEDULE B |
| --- | --- |

RFQ Title:	Supply and Delivery of One or More 4WD Agricultural Tractor

RFQ No:	1220-040-2019-007

CONTRACTOR

Legal Name:

Contact Person and Title:

Business Address:

Business Telephone:

Business Fax:

Business E-Mail Address:

CITY OF SURREY

TO:

City Representative:	Richard D. Oppelt, Purchasing Manager

Address:		Surrey City Hall

Finance Department – Purchasing Section

Reception Counter, 5th Floor West

13450 – 104th Avenue, Surrey, BC  V3T 1V8

Telephone:	604-590-7274

Email:	purchasing@surrey.ca

1.	The Contractor offers to supply to the City of Surrey the Goods for the prices plus applicable taxes as follows:

Year, Make & Model:  __________________________________________________________

All costs to meet the preferred specifications shall be included in the following delivered prices.

| F.O.B. | Payment Terms: | Ship Via: |
| --- | --- | --- |
| Destination Freight Prepaid | A cash discount of ____% will be allowed if invoices are paid within ___ days, or the ___ day of the month following, or net 30 days, on a best effort basis. |  |
| ITEM | 4WD AGRICULTURAL TRACTOR |
| VEHICLE QUANTITY |  |
| AGRICULTURAL TRACTOR ENVIRONMENTAL LEVY [BATTERY] | $ $ |
| TIRE STEWARDSHIP B.C. (TSBC) | $ |
| OTHER: |  |
| ____________________________ | $ |
| ____________________________ | $ |
| ____________________________ | $ |
| SUBTOTAL | $ |
| GST 5% | $ |
| PST 7% | $ |
| TOTAL QUOTED PRICE: | $ |
| CURRENCY: CANADIAN |  |

The completed unit shall be delivered within _______ days after receipt of purchase order.

Manufacturer’s Warranty:  State Warranty

Body Warranty:  State Warranty________________________________________________________

Warranty repairs shall be performed at

Please complete if applicable:	British Columbia Certified (

SPECIFICATIONS

The specification herein states the preferred requirements of the City of Surrey. All Quotations are regular in every respect. Unauthorized conditions, limitations, or provisions may be cause for rejection. The City of Surrey will consider as "irregular" or "non-responsive" any Quotation not prepared and submitted in accordance with the RFQ document and specification, or any Quotation lacking sufficient technical literature to enable the City to make a reasonable determination of compliance to the specification.

It shall be the Contractor's responsibility to carefully examine each item of the specification. Failure to offer a completed Quotation or failure to respond to each section of the technical specification may cause the Quotation to be rejected without review as "non-responsive". All variances, exceptions and/or deviations shall be fully described in the appropriate section.

Note: Contractors are directed to list complete manufacturers’ details of model proposed in the right-side column under manufacturers’ specifications

| Preferred Specifications | √ (Yes) | √ (No) | Manufacturers’ Specifications of Equipment offered. Contractor shall complete all spaces in this column. |
| --- | --- | --- | --- |
| ENGINE |
| 1.1 Shall be minimum of 70HP 4 - cylinder engine with high pressure common rail fuel system | □ | □ |  |
| 1.2 Complies with Tier 4 emission standard | □ | □ |  |
| 1.3 Permanent pre-cleaner and safety element shall be provided | □ | □ |  |
| 1.4 Under hood after treatment system | □ | □ |  |
| 1.5 Minimum of 90 litre fuel tank | □ | □ |  |
| TRANSMISSION |
| 2.1 12F/12R with forward/reverser shuttle shall be provided. Transmission shall be fully synchronized with high & low speed selector. | □ | □ |  |
| 2.2 Clutch shall be wet multi disc | □ | □ |  |
| 2.3 Park lock/brake shall be provided | □ | □ |  |
| 2.4 For safety, a neutral safety start system shall be included | □ | □ |  |
| 2.5 4WD to be engaged and disengaged via an electro hydraulic switch | □ | □ |  |
| STEERING, BRAKES, DIFFERENTIAL, FRAME |
| 3.1 Unit shall be equipped with hydrostatic steering | □ | □ |  |
| 3.2 Hydraulic wet disc brakes shall be provided | □ | □ |  |
| 3.3 Rear axle should have differential lock | □ | □ |  |
| 3.4 Front differential shall be limited slip | □ | □ |  |
| HYDRAULICS/PTO |
| 4.1 A load sensing constant flow system shall be provided | □ | □ |  |
| 4.2 Minimum of 60 litres /min | □ | □ |  |
| 4.3 Rear independent PTO shall be 540 RPM | □ | □ |  |
| 4.4 There shall be 3 hydraulic valves at the rear of the tractor for operating towed implements | □ | □ |  |
| 4.5 Category I/II 3 – point hitch with telescopic top link and telescopic stabilizers | □ | □ |  |
| 4.6 Control system, top link load sensing | □ | □ |  |
| 4.7 Lift capacity @ 24” a minimum of 1500 kgs | □ | □ |  |
| INSTRUMENTATION |
| 5.1 Display functions definable by operator shall include: |  |  |  |
| 5.2 Ground speed | □ | □ |  |
| 5.3 PTO speed | □ | □ |  |
| 5.4 Engine hours | □ | □ |  |
| 5.5 Service hours | □ | □ |  |
| 5.6 Fuel gauge | □ | □ |  |
| 5.7 Engine oil pressure indicator light/gauge | □ | □ |  |
| 5.8 Coolant temperature | □ | □ |  |
| 5.9 PTO engagement | □ | □ |  |
| 5.10 Alternator indicator light | □ | □ |  |
| 5.11 Directional indicators | □ | □ |  |
| 5.12 Hazard switch | □ | □ |  |
| CAB OPERATOR STATION |
| Cab shall be ROPS and equipped with: |
| 6.1 Manually adjustable left and right rear vision mirrors |  |  |  |
| 6.2 Air conditioning and heater | □ | □ |  |
| 6.3 Two doors | □ | □ |  |
| 6.4 Front windshield wiper and washer | □ | □ |  |
| 6.5 Rear windshield wiper and washer | □ | □ |  |
| 6.6 Air suspension seat | □ | □ |  |
| 6.7 Arm rests and seat belt | □ | □ |  |
| 6.8 Tilt/telescopic steering column | □ | □ |  |
| 6.9 Right hand operator controls | □ | □ |  |
| 6.10 Floor mat | □ | □ |  |
| 6.11 Foot throttle control | □ | □ |  |
| 6.12 12-volt power outlet | □ | □ |  |
| 6.13 AM/FM/CD radio | □ | □ |  |
| 6.14 Overhead courtesy light | □ | □ |  |
| 6.15 Rear view mirror | □ | □ |  |
| 6.16 Cup holder | □ | □ |  |
| 6.17 Sun visor | □ | □ |  |
| ELECTRICAL: |
| 7.1 A minimum of a 60-amp alternator shall be provided | □ | □ |  |
| 7.2 Headlights shall be provided | □ | □ |  |
| 7.3 Two front outer roof work lights | □ | □ |  |
| 7.4 One rear right roof work light | □ | □ |  |
| 7.5 Four roof mounted flashing hazard lights | □ | □ |  |
| 7.5 Back up alarm shall be provided | □ | □ |  |
| 7.6 Two rear fender stop, tail indication lights, with “hazard function” | □ | □ |  |
| 7.7 Beacon light – Falcon mini bar part # F84AWB4-YY. To be mounted on cab to left side towards the rear. | □ | □ |  |
| AXLES, WHEELS AND TIRES: |
| 8.1 4WD front axle with electro-hydraulic engagement shall be supplied | □ | □ |  |
| 8.2 Front and rear tires shall be a “turf tire type” – please provide details | □ | □ |  |
| 8.3 Width of tire and rim shall be of a width to minimize any damage the turf/playing fields – please provide details | □ | □ |  |
| 8.4 The tire size shall ensure the tractor has a minimum road speed of 40kph | □ | □ |  |
| WARRANTY |
| 9.1 There shall be a minimum 1-year parts and labor warranty on the tractor. | □ | □ |  |
| 9.2 Please provide details on extended warranty and costs | □ | □ |  |
| OPERATOR PROTECTION & SAFETY |
| 10.1 A slow moving vehicle sign to be mounted in prominent position on the rear of the tractor | □ | □ |  |
| 10.2 1 - 2lb dry powder fire extinguisher shall be provided | □ | □ |  |
| 10.3 1 – No.1 first aid kit shall be provided | □ | □ |  |
| 10.4 An audible back-up alarm of approx. 98 dbh shall be provided | □ | □ |  |
| STANDARDS |
| 11.1 Tractor must comply with government regulations and requirements which allow it to operate on roads and highways. |
| Federal government motor vehicle standards BC motor vehicle act and regulations BC workers’ compensation board regulations BC emissions standards |  |  |  |
| MISCELLANEOUS |
| 12.1 3 full sets of keys shall be provided | □ | □ |  |
| 12.2 Manufacturer’s Certificate of Origin shall be provided | □ | □ |  |
| 12.3 One complete Service Manual shall be provided | □ | □ |  |
| 12.4 One complete Parts Manual shall be provided | □ | □ |  |
| 12.5 A complete parts list shall be provided for belts, filters, and hoses | □ | □ |  |
| 12.6 Fluid capacities in litres | □ | □ |  |
| 12.7 The tractor shall be delivered, registered and insured. The insurance shall be arranged through the City of Surrey’s insurance broker. | □ | □ |  |

2.	In addition to the warranties provided in the Draft Quotation Agreement, this Quotation includes the following warranties:

3.	I/We have reviewed the RFQ Attachment 1, Schedule A – Specifications of Goods and if requested by the City, I/we would be prepared to meet those requirements, amended by the following departures and additions (list, if any):

Requested Departure(s) / Alternative(s) / Addition(s)

The City is not obligated to accept any alternatives. The City will determine what constitutes acceptable deviations and overall best value.

4.	If this Quotation is accepted by the City, a contract will be created as described in:

(a)	the Agreement;

(b)	the RFQ; and

(c)	other terms, if any, that are agreed to by the parties in writing.

5.		Capitalized terms used and not defined in this Quotation will have the meanings given to them in the RFQ.  Except as specifically modified by this Quotation, all terms, conditions, representations, warranties and covenants as set out in the RFQ will remain in full force and effect.

6.	I/We have reviewed the RFQ Attachment 1 – Draft Quotation Agreement.  If requested by the City, I/we would be prepared to enter into that Agreement, amended by the following departures (list, if any):

Section			Requested Departure(s) / Alternative(s)

7.	I/We the undersigned duly authorized representatives of the Contractor, having received and carefully reviewed the RFQ including without limitation the specifications and the General Terms and Conditions, submit this Quotation in response to the RFQ.

This Quotation is offered by the Contractor this _______ day of _______________, 201_.

CONTRACTOR

I/We have the authority to bind the Contractor

| ________________________________________ (Legal Name of Contractor) _________________________________________ (Signature of Authorized Signatory) _________________________________________ (Print Name and Position of Authorized Signatory) | ________________________________________ (Signature of Authorized Signatory) ________________________________________ (Print Name and Position of Authorized Signatory) |
| --- | --- |

Updated:  May 2016

MAY 21, 2009

U:\LEGALSRV\LEGAL\AGREEMENTS\RFP-Contract-Templates\Documents\Request for Quotations for Goods.doc

saw\lb1-1/11/19 12:53 PM